## Slide 1
Synchronization Between Sensors and Cameras in Movement Data Labeling Frameworks
Jacob Kamminga, Michael Jones, Kevin Seppi, Nirvana Meratnia, Paul Havinga

## Slide 2: Introduction
Obtaining labeled data is a tedious and daunting task
Ground truth often collected using video that record subjects wearing sensors
During labeling sensor-data preferably synchronized with video and displayed simultaneously

## Slide 4: Approach Comparison
Approach A: Synchronization using visual key
Approach B: Synchronization using real-time clocks
Notes: We compared two frameworks

## Slide 5: Approach A

## Slide 6: Approach A: Synchronization using visual key
Data logger emits flash and timestamps sensor-data stream
The first video frame that contains flash is marked by user
1 subject per recording
Synchronization must be repeated for each video
Notes: This is fine when recording human subjects one by one. Animals however different approach

## Slide 7: Approach B: Synchronization using real-time clocks
Assumes camera and datalogger both contain RTC
RTC coarsely synchronized prior to experiments

## Slide 8: Approach B: Synchronization using real-time clocks
Synchronize on distinctive event in the video and adjust offset σ(l)m,n between a given camera m and sensor n on day l
shake sensors before camera during sync-recording

## Slide 9: Comparison
Approach | Advantages | Disadvantages
A: visual key | High accuracy | Only one subject per recording
 |  | Each video must be synchronized individually
B: RTC | Sync only once | Lower accuracy
 | Multiple subjects in one video Easier to collect more data in parallel Higher chance to record rare activity | Susceptive to clock drift
 | Easier to use multiple cameras simultaneously | 
 | Dataloggers can be post-synchronized among each-other | 

## Slide 10: Conclusion
Timestamped visual keys on the datalogger result in accurate synchronization between sensors data and video
Using RTC for synchronization allows to monitor multiple subjects simultaneously on same video

## Slide 11: Ideas
Best idea seems to combine both approaches
Use visual keys on datalogger for both sensor identification and synchronization
Automatic synchronization by encoding time information in blinking pattern

## Slide 12: Thanks for your attention
Synchronization Between Sensors and Cameras in Movement Data Labeling Frameworks
Jacob Kamminga, Michael Jones, Kevin Seppi, Nirvana Meratnia, Paul Havinga